## Slide 1: Thesis Defense: Analysis of Various Algorithmic Approaches to Software-Based APRS Packet Demodulation
By: Robert Campbell
Committee Members: Dr. John Bellardo, Dr. Bridget Benson, and Dr. Dennis Derickson
Notes: Introduce People in the room

## Slide 2: What is APRS?
Automated Packet Reporting System.
A digital communication method used by hams.
Encoded into the Radio Using Bell 202
Notes: Discuss Digital vs Analog Communication. Ironic note about how APRS is both.
Packet content can be many things but most commonly is a GPS position.
Mention that Bell 202 is the key to this research (not too much detail about what it is since that will be covered later)

## Slide 3: What does APRS look like?
Notes: AGWTracker, AGWPE, Wildflower, course maps.

## Slide 4: What does APRS look like?
Notes: Walk through of APRS.fi show:
-Stations
-Tracks
-Messages
-Telemetry

## Slide 5: Bell 202
1200 Baud AFSK using 1200Hz and 2200Hz tones.
Audio Frequency Shift Keying – using multiple tones in the audible range to encode data.

## Slide 6: Example Signal
Notes: 1200Hz and 2200Hz tones.
Since 2200Hz doesn’t divide evenly in a 1200 baud bit period you can see that it changes the phase.

## Slide 7: It’s in the audible range
What’s it sound like?
Notes: Play Example APRS packet
Brief introduction to flags. Data is only contained in 0.5s worth of the audio file.

## Slide 8: How to demodulate this signal?
Edge Detection
Correlation
Filters
Phase Locked Loop
Notes: These approaches are shared in both hardware and software based approaches.

## Slide 9: Edge Detection
Look for rising and falling edges
Distance between consecutive “zero-crossings” is λ/2

## Slide 10: Correlation
Correlates original signal with expected signals.

## Slide 11: Filters
Filters look at signal strength of individual frequencies.

## Slide 12: Phase Locked Loop (PLL)
Phase lock is acquired on the original signal.
As long as the VCO is locked the signal is known.

## Slide 13: Approaches to Accessing the Network
Terminal Node Controllers
Specialty APRS Hardware
Radio Integrated
Software

## Slide 14: TNC Examples

## Slide 15: Argent Data Open Trackers

## Slide 16: Radio Integrated APRS

## Slide 17: AGWPE

## Slide 18: javAX25 in APRSdroid

## Slide 19: Challenges
DC Offset
Noise
Emphasis

## Slide 20: DC Offset

## Slide 21: Noise

## Slide 22: Emphasis

## Slide 23: Algorithms Implemented
Zero Crossing
Goertzel (DFT / Filtering)
PLL
Preclocking

## Slide 24: Zero Crossing

## Slide 25: Goertzel (DFT / Filtering)

## Slide 26: PLL

## Slide 27: Preclocking

## Slide 28: Benchmarking
OT3 Test
javAX25 Generated 200
OT3 Test + Ramping Noise
Track 1
Track 2

## Slide 29: Clean Signal Example

## Slide 30: Noise Example

## Slide 31: Track 1 Example

## Slide 32: Hardware Results - Clean

## Slide 33: Hardware Results - Noise

## Slide 34: Hardware Results – Track 1

## Slide 35: Software Results - Clean

## Slide 36: Software Results - Noise

## Slide 37: Software Results – Track 1

## Slide 38: Hardware versus Software

## Slide 39: Ideas for Future Work

## Slide 40: Conclusion