## Slide 1: Thesis Defense: Analysis of Various Algorithmic Approaches to Software-Based APRS Packet Demodulation
By: Robert Campbell
Committee Members: Dr. John Bellardo, Dr. Bridget Benson, and Dr. Dennis Derickson
Notes: Introduce People in the room

## Slide 2: What is APRS?
Automated Packet Reporting System.
A digital communication method used by hams.
Encoded into the Radio Using Bell 202
Notes: Discuss Digital vs Analog Communication. Ironic note about how APRS is both.
Packet content can be many things but most commonly is a GPS position.
Mention that Bell 202 is the key to this research (not too much detail about what it is since that will be covered later)

## Slide 3: What does APRS look like?
Notes: AGWTracker, AGWPE, Wildflower, course maps.

## Slide 4: What does APRS look like?
Notes: Walk through of APRS.fi show:
-Stations
-Tracks
-Messages
-Telemetry

## Slide 5: Approaches to Accessing the Network
Terminal Node Controllers
Specialty APRS Hardware
Radio Integrated
Software

## Slide 6: TNC Examples
Notes: Pass around examples, show that there is a radio port and COM port that can be found on each.

## Slide 7: Argent Data Open Trackers

## Slide 8: Radio Integrated APRS

## Slide 9: AGWPE

## Slide 10: javAX25 in APRSdroid

## Slide 11: The Sine Wave
y(t) = A sin(2πft + φ)
f = 1 (f = 1/T)
A = 1
φ = -π/4
Chart: 
A
φ
T
Notes: Frequency is in Hertz
Frequency and Period are Inverse. Longer (larger) period is a lower (smaller) frequency, Shorter period is a higher (larger) frequency.
Phi is the phase

## Slide 12: Bell 202
1200 Baud AFSK using 1200Hz and 2200Hz tones.
Audio Frequency Shift Keying – using multiple tones in the audible range to encode data.
Notes: Introduce Frequency Shift Keying
A patent for the modem chip to modulate and demodulate the digital data was filed in 1981
V.23 with 1300Hz and 2100Hz tones in 1988

## Slide 13: Example Signal
Notes: 1200Hz and 2200Hz tones.
Since 2200Hz doesn’t divide evenly in a 1200 baud bit period you can see that it changes the phase.

## Slide 14: It’s in the audible range
What’s it sound like?
Notes: Play Example APRS packet
Brief introduction to flags. Data is only contained in 0.5s worth of the audio file.

## Slide 15: How to demodulate this signal?
Edge Detection
Correlation
Filters
Phase Locked Loop
Notes: These approaches are shared in both hardware and software based approaches.

## Slide 16: Edge Detection
Look for rising and falling edges
Distance between consecutive “zero-crossings” is T/2
Chart: 
T/2
T/2
Notes: Mention that this method is especially susceptible to the challenges to be presented later.

## Slide 17: Correlation
Correlates original signal with expected signals.
Notes: S1 and s2 are the 1200Hz and 2200Hz signals

## Slide 18: Filters
Filters look at signal strength of individual frequencies.
Notes: h1(t) and h2(t) are the outputs from applying the respective filters at 1200Hz and 2200Hz

## Slide 19: Phase Locked Loop (PLL)
Phase lock is acquired on the original signal.
As long as the VCO is locked the signal is known.
Notes: Incoming signal is mixed with the output from the VCO (Voltage Controlled Oscillator)
Phase is filtered then passed back to the VCO
Phase / Frequency information is used to decide which frequency is present.

## Slide 20: Challenges
DC Offset
Noise
Emphasis
Notes: These are just some examples of challenges that were encountered during this research.
Other challenges include:
-RF Limitations including limited coverage
-Multiple stations transmitting at the same time

## Slide 21: DC Offset
Notes: Notice that the average is above zero
Notice the zero crossings are not even

## Slide 22: Noise
Notes: The jitter may cause one signal to look like another extending or shortening zero crossings.

## Slide 23: Emphasis
Notes: This is a challenge for any filter because it can not be assumed that the relative magnitudes of the signals are the same.

## Slide 24: Algorithms Implemented
Zero Crossing
Goertzel (DFT / Filtering)
PLL
Preclocking

## Slide 25: Zero Crossing
Zero Crossing
Strict Zero Crossing
Windowed Zero Crossing
Peak

## Slide 26: Strict Zero Crossing
if ((isSignalHigh && isBelowZero(sample))
|| (!isSignalHigh && isAboveZero(sample))) {
  handleZeroCrossing();
  isSignalHigh = !isSignalHigh;
}

## Slide 27: Zero Crossing
//going low to high
if ((!wasSignalHigh && sample > averageValueInHistory + zeroCrossingThreshold)||
//going high to low
(wasSignalHigh && sample <
averageValueInHistory - zeroCrossingThreshold))
{
handleZeroCrossing();
wasSignalHigh = !wasSignalHigh;
}
Notes: Notice the adujustable “zero”

## Slide 28: Goertzel (DFT / Filtering)
double power = (s1200_prev2*s1200_prev2+s1200_prev*s1200_prev-coeff1200*s1200_prev*s1200_prev2) -
(s2200_prev2*s2200_prev2+s2200_prev*s2200_prev-coeff2200*s2200_prev*s2200_prev2);
Notes: Only multiplication and addition no other complicated computations i.e. integrals or sines

## Slide 29: Goertzel Trial Run in MATLAB
Notes: This is on the OT3 Test with noise.

## Slide 30: PLL
// Mix VCO with incoming signal
double pll_loop_control = sample * ref_sig * pll_loop_gain;
// Filter
double output = biQuad.filter(pll_loop_control);
pll_integral += pll_loop_control / sample_rate;
// Update VCO
ref_sig = (float) Math.sin(2 * Math.PI * pll_cf * (t + pll_integral));
if ((output > 0 && !lastGreaterThanZero) ||
(output < 0 && lastGreaterThanZero)) {
  handleFrequencyChange()
}

## Slide 31: Preclocking
Look for flags to determine start and end of packet
Find all the transitions in the packet
Using the transitions found determine the clocking
Demodulate each baud one at a time

## Slide 32: Benchmarking
OT3 Test
javAX25 Generated 200
OT3 Test + Ramping Noise
Track 1
Track 2

## Slide 33: Clean Signal Example

## Slide 34: Noise Example

## Slide 35: Track 1 Example

## Slide 36: The Big Tables-O-Data
.wav file | Filtering | Correlation | Zero Crossing | Strict Zero Crossing | Windowed Zero | Peak | Derivative | Goertzel (100%) | Goertzel Optimized window | PLL | PreClocking | Goertzel PreClocking | Goertzel Max Preclocking | AGWPE | AVERAGE HARDWARE
OT3Test | None | 40 | 35 | 40 | 39 | 3 | 40 | 40 | 40 | 40 | 0 | 40 | 40 | 40 | 39.9166667
 | Bandpass | 40 | 19 | 0 | 0 | 0 | 33 | 40 | 40 | 40 | 40 | 28 | 40 |  | 
 | Bandpass w/ 6db | 40 | 12 | 40 | 0 | 0 | 14 | 40 | 40 | 0 | 39 | 15 | 40 |  | 
SoftwareGenerated200 | None | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 0 | 200 | 200 | 200 | 199.272727
 | Bandpass | 200 | 27 | 200 | 0 | 0 | 200 | 200 | 200 | 200 | 200 | 106 | 200 |  | 
 | Bandpass w/ 6db | 200 | 200 | 200 | 0 | 0 | 200 | 200 | 200 | 200 | 200 | 199 | 200 |  | 
OT3TestWithNoise | None | 24 | 0 | 6 | 0 | 0 | 3 | 17 | 25 | 21 | 0 | 10 | 27 | 21 | 14.5833333
 | Bandpass | 24 | 6 | 2 | 0 | 0 | 5 | 21 | 23 | 23 | 17 | 11 | 26 |  | 
 | Bandpass w/ 6db | 11 | 1 | 9 | 0 | 0 | 4 | 8 | 6 | 14 | 6 | 5 | 18 |  | 
LATrack1 | None | 946 | 460 | 568 | 298 | 0 | 543 | 935 | 965 | 925 | 0 | 564 | 806 | 967 | 935.083333
 | Bandpass | 964 | 536 | 151 | 0 | 0 | 422 | 941 | 965 | 654 | 939 | 431 | 813 |  | 
 | Bandpass w/ 6db | 914 | 53 | 422 | 0 | 0 | 97 | 613 | 512 | 189 | 482 | 224 | 795 |  | 
LATrack2 | None | 639 | 0 | 0 | 162 | 0 | 5 | 411 | 608 | 0 | 0 | 390 |  | 497 | 777.916667
 | Bandpass | 872 | 0 | 0 | 0 | 0 | 0 | 401 | 448 | 0 | 939 | 230 |  |  | 
 | Bandpass w/ 6db | 958 | 209 | 74 | 0 | 0 | 254 | 946 | 956 | 0 | 947 | 392 |  |  | 
.wav file | AVERAGE HARDWARE | OT2 | OT3 | OT USB | OT3 Micro | Kam | My Kam Plus | Kam Plus | MFJ-1278 | My PK-88 | PK-88 | PK-232 | PK-232MBX
OT3Test | 39.9166667 | 40 | 40 | 39 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40
SoftwareGenerated200 | 199.272727 | 200 | 200 | 193 | 199 | 200 | 200 | 200 | 200 | 200 |  | 200 | 200
OT3TestWithNoise | 14.5833333 | 5 | 16 | 13 | 12 | 20 | 12 | 12 | 5 | 25 | 25 | 12 | 18
LATrack1 | 935.083333 | 947 | 937 | 869 | 830 | 988 | 958 | 985 | 837 | 981 | 1007 | 918 | 964
LATrack2 | 777.916667 | 927 | 445 | 633 | 263 | 938 | 967 | 998 | 937 | 866 | 633 | 929 | 799
Notes: Talk about where the hardware results came from

## Slide 37: Hardware Results - Clean
Only Hardware that did not decode all packets was:
  OpenTracker USB with 39/40 and 193/200
  T3-Micro 199/200
Notes: All other 10 pieces of hardware decoded 40 and 200 packets out of the respective files.

## Slide 38: Hardware Results - Noise

## Slide 39: Hardware Results – Track 1

## Slide 40: Software Results - Clean

## Slide 41: Software Results - Noise

## Slide 42: Software Results – Track 1

## Slide 43: Hardware versus Software
Notes: All the software is on the left (sad )
Average for hardware was 935, All of these software are above that

## Slide 44: Ideas for Future Work
The Discrete Short-Time Fourier Transform
Use the CRC for FEC
Integrations with a Radio
Notes: Came across paper of DSTFT look like it had good results with fast computation times even in noisy signals

## Slide 45: Closing Comments & Questions
Notes: The software didn’t end up doing as good as hardware (still)
Some quote about just finding some ways that didn’t make it better. Software is limitless and there are many ways left to try.
Software is a good cost effective alternative! Hardware components ware out while software is consistent